## Slide 1
Austin Gnecco1, Tyler Johnson2+
Introduction
Conclusions
Acknowledgments
Design
FPGA Based
BiSS C Splitter
1Your Affiliation.
2Linac Coherent Light Source, SLAC National Accelerator Laboratory, 2575 Sand Hill Road, Menlo Park, CA 94025, USA.
+Contact: tjohnson@slac.stanford.edu
Date: 9/10/2020
The problem that I was tasked with was to find a way to record the information from a closed loop encoder system, so that it could be monitored by the greater LCLS beamline control system. Currently, there are extremely precise encoders on the LCLS mirror tables, however, they only communicate with their attached motor, and do not offer a native option to record position data.
The proposed solution was to design a FPGA based signal splitter, to be used with the encoders on the aiming tables at LCLS. The job of this signal splitter is to take the position information from the encoder and (upon request) deliver that information to either the control motor or a data acquisition device to log its position or report it to the greater control system.
I approached this design by first creating a simulation in MATLAB, and then using that simulation to generate the VHDL code that will be used to run the splitter. The VHDL code will then be applied to a Artix-7 development board, to split the signals.
Although the final implementation of this code is ongoing, the MATLAB simulations have shown that this splitter design is capable of quickly and accurately storing data to be shared between two different devices.
This design will be further validated through simulation of the generated VHDL code using Vivado before it will be tested on the actual encoder, motor and DAQ hardware at LCLS.
The ability for LCLS operators to log and verify the positions of mirrors on the beamline should allow for a more complete view of beamline operations.
Use of the Linac Coherent Light Source (LCLS), SLAC National Accelerator Laboratory, is supported by the U.S. Department of Energy, Office of Science, Office of Basic Energy Sciences under Contract No. DE-AC02-76SF00515.
Many potential designs were created, but eventually the one that was settled on used two banks of memory that would be switched between to provide the most accurate position information. The design works as such:
The encoder and motor use a protocol called BiSS-C in order to communicate (Fig. 1). In this protocol, an MA signal is sent from the commanding device to act as a clock. It is a square wave that can range anywhere between 1mhz and 10mhz. As not every device is required to use the same frequency, the splitter had to be capable of dealing with multiple clock speeds at the same time.
All interactions with the encoder are controlled through the BiSS-C Master Module(Fig. 3). This module continuously sends a 10 MHz square wave to the encoder, in order to get new location data as often as possible. As the information is received back from the encoder, this module also counts the number of bits received and looks for errors before passing the information on to the buffer module.
Upon the encoder signals entering the Buffer Module (Fig. 4), the Task Scheduler (Fig. 5) looks at all of the different signals coming in and decides which requests will be executed first. The DAQ and Motor BiSS C Slave modules (shown in Fig. 2) process requests from
MATLAB Design
Fig.1 – BiSS-C Waveform
Fig. 2 – System Overview
Fig. 3 – BiSS C Master Module
Fig. 4 – Buffer Module
Fig. 5 – Task Scheduler
the DAQ and motor and send signals to the Task Scheduler when they request new encoder location data.
Read requests from the motor have the highest priority over any action and will be executed first. If there is also a request to write new information from the encoder at the same time as a request to read information, the two events can happen simultaneously. This is because there are two banks of data. When new information from the encoder is received, it is written to bank 1. While new data is being written, the old data can be read off bank 2, to either the motor or the DAQ. Assuming that no errors are detected the banks then switch, making bank 2 the most recent information that is send out of the device, while bank one is written over with new information from the encoder. If an error is detected, the banks do not switch, and the corrupt data is written over by new data, before it becomes the new data to be read.
This structure ensures that the information being sent out can be as recent and accurate as possible, while still allowing for the encoder, motor, and DAQ to all read and write data at their own preferred clock speed.
Design Continued